## Slide 1: OCCUPATIONAL ERGONOMICS
Chapter 7
COGNITIVE ERGONOMICS

## Slide 2: INFORMATION PROCESSING
Learning Objectives
At the conclusion of this chapter, learners will be
able to do the following:
  Classify types of memory and attention resources
  Describe principles of human-machine interface
  Demonstrate understanding of information coding by humans
  Describe methods to evaluate and design user instructions and warnings

## Slide 3: INFORMATION PROCESSING
Introduction
  Previous chapters: physical, physiological and some perceptual aspect of work.
  This chapter: cognitive and mental processing for effective design of workplaces.
  Other terms used: cognitive psychology, cognitive engineering or engineering psychology

## Slide 4: INFORMATION PROCESSING
Cognitive Models
  Various models available for understanding human behavior and other psychological attributes
  This chapter: deals with basic cognitive and human factors related to work systems
  Though criticized as inadequate, one such theory of information processing provides adequate platform for engineers to design work systems

## Slide 5: INFORMATION PROCESSING
Coding of Information
Much of the information available for
processing by human brain is coded in one form or the other.
Or it is packaged to suit the end user.
Effectiveness of information transfer is dependent upon the ability to code information effectively as well as the ability by the end user to accurately decipher it.

## Slide 6: INFORMATION PROCESSING
Role of Memory
Human memory is thought to have three sub-systems or processes:
    Sensory storage
    Working memory (often referred to as short-term memory), and
    Long-term memory
  All sensory systems have got storage capacity,
  which is automatic and there is no evidence to
  suggest that it can be increased

## Slide 7: INFORMATION PROCESSING
Role of Memory
Human memory is thought to have three sub-systems or processes:
    Sensory storage
    Working memory (often referred to as short-term memory), and
    Long-term memory
  All sensory systems have got storage capacity,
  which is automatic and there is no evidence to
  suggest that it can be increased

## Slide 8: INFORMATION PROCESSING
Describes activities that occur between
stimulus input and response output.
Three basic processes:
  Encoding
  Storage
  Retrieval

## Slide 9: INFORMATION PROCESSING (contd.)
Attention: stimulus that are most salient or relevant to one at the time or that evoke most emotion tend to harness our attention most.
Sensation: the mechanism people use to process physical energy that impinges on their sensory organs.
Perception: the process of interpreting the stimuli.

## Slide 10: INFORMATION PROCESSING (contd.)
Attention
  Selective Attention: refers to situation where a person is monitoring multiple “channels” of information. e.g., a pilot monitoring numerous instruments in addition to situation external to the aircraft.
  Focused Attention: refers to situation which requires that attention be maintained on or (or very few similar) channels while not being distracted by other sources of information.

## Slide 11: INFORMATION PROCESSING (contd.)
Attention
  Divided Attention: refers to situation where more than one task is attended to. There is performance degradation due to pooling of attention available at any time to an individual.
  Sustained Attention: refers to the ability of a worker to maintain attention and remain alert to the presence of certain information for prolonged periods of time.

## Slide 12: INFORMATION PROCESSING (contd.)
Effects of Aging on Attention
  Performance in many cognitive tasks will be generally reduced within the aged populations (generally over 65 years of age). Such changes will include:
    Slowing of information retrieval from LTM
    Slowing of response time in selecting alternatives
    Slowing of execution time with responses
    Increase in disruptions in working memory
    Increased difficulty in dealing incompatibility in sensory information, and
    Decrement in perceptual encoding.

## Slide 13: INFORMATION PROCESSING (contd.)
Memory
  Atkinson-Shiffrin Model of Memory
    Sensory register
    Short - term memory
    Working memory
    Long - term memory
      Semantic
      Episodic
      Procedural

## Slide 14: INFORMATION PROCESSING (contd.)
Forgetting and Long-term Memory
  Decay Theory: all else being equal, information that is used frequently is more readily available for recall than information used infrequently.
  Neural network model: this also supports the decay theory.
  Interference

## Slide 15: INFORMATION PROCESSING (contd.)
Resource Theory:
  User has only a limited amount of resources with which to operate at any given time
Human Machine Interface
  The human interacts with the controls and displays of the machine in achieving some objective.

## Slide 16: CONTROLS AND DISPLAYS
Control: is a device by which an operator
interacts with the environment. It allows a
person to change the status of a system.
Important considerations in the design and
selection of control devices include the
following:
  Types of control
    Discrete action control: has mutually exclusive engagement, e.g., push buttons, membrane switches, toggle switches, rotary detent switches, etc.

## Slide 17: CONTROLS AND DISPLAYS
    Continuous action control: e.g., rotary knobs, slide switches, foot pedals, joysticks, computer mouse and other pointing devices.
  Feedback: process by which operators know what actions or accomplishments their inputs are having on the system
  Control resistance
    Engineering specs. that minimize accidental activation
    Should also minimize operator fatigue

## Slide 18: CONTROLS AND DISPLAYS
  Location
    Should not cause awkward positioning of body
    Frequently used controls should be within normal reach envelope.
  Size and shape
    Should be compatible with the hand size
    Implications of attire and/or couplings
    Implications for appropriate grasp
    Consideration should include location of adjacent controls

## Slide 19: CONTROLS AND DISPLAYS
  Interface surface
    Depends on required operation (knurled for precise movement could interfere with power grasp)
  One versus two-handed operations
    One handed should be used if no large forces are required or if other hand is needed for manipulation of another control.

## Slide 20: CONTROLS AND DISPLAYS
Displays: are prime source of feedback for the operator in the control of a system. They allow a person to monitor the status of a system.
User Expectation: designer’s design decision should be consistent with what the user expects. When the expectations are not obvious, a study should be conducted to determine what the expectations are.

## Slide 21: CONTROLS AND DISPLAYS (contd.)
Types of Displays
  Visual: can be broken down into
    Visual Signal Detection, and
    Information transfer
    Visual Signal Detection: it refers to warning
    lights, which are often coupled with auditory
    warnings to attract the attention of the operator.
    They should have the following characteristics:
      Signal should flash with an “on” duration of at least 0.05 sec and a frequency of 3 to 10 Hz
      Signal should be marked with visual command
      Should be of difference luminance than the immediate background

## Slide 22: CONTROLS AND DISPLAYS (contd.)
      Should not be subject to confusion due to color
      Should be located within normal visual workspace.
    Visual Displays for Information Transfer: when an operator examines a display after the attention is drawn, the information should be quickly readable and understandable so that required action could be taken immediately. The following are the design guidelines:
      Select the simplest design requiring minimum level of precision
      Design and select for expectancy
      Optimize display characteristics such as visibility, conspicuousness, legibility, and interpretability

## Slide 23: CONTROLS AND DISPLAYS (contd.)
  Auditory Displays: can also be divided into:
    Signal detection, and
    Information transfer
    Design guidelines are:
    Signals work best when accompanying a visual display
    Avoid using multiple auditory signals
    Avoid using in noisy environment
    Signal should be at least 15 dB above the surrounding

## Slide 24: CONTROLS AND DISPLAYS (contd.)
    The following characteristics should be considered:
      Pitch should be between 400 and 1500 Hz
      Signal should have at least four prominent frequency component to minimize masking by other noises
      Rapid gliding in the frequency can be used to make it stand out
    Avoid annoyance:
      Very loud signals
      Signals that are frequently used

## Slide 26: INSTRUCTIONS
  Instructions should be clear and concise and should answer the following questions
    Who are the users?
    What is the relative importance of each instruction?
    What is the proper location for the instructions?
    How much information redundancy is important?
    What is the most effective method and format of presentation (text, diagrams, photographs, etc.)?
    How intelligible are the instruction, and is the nomenclature appropriate?

## Slide 27: INSTRUCTIONS
Guidelines for developing instruction sets
  Sequence of instruction should follow sequence of required actions
  Short sentences, flow diagrams, algorithms, lists, and tables are superior to plain text
  Best to use active tense and affirmative sentence
  Should be integrated into equipment or production work forms than on separate forms
  Format is situation dependent
  Should be tested on naïve users before finalizing

## Slide 28: LABELS AND SIGNAGE
Labels and signage: Typically used to convey
much shorter messages about a more specific
topic
Factors in the design of labels and signs
  Comprehensibility
    Clearly have in mind the purpose and intended meaning of the message
    Orient wording directed toward the least knowledgeable foreseeable user population
    Brief and concise to avoid ambiguity
    Standardize whenever possible
    Use symbols and icons whenever possible

## Slide 29: LABELS AND SIGNAGE
  Legibility
    Use simple fonts
    Recommended proportion of text
      Character width: 2/3 of character height
      Stroke width: 1/6 of character height
      Spacing (leading): 1/5 of character height
      Spacing between text and figures: 2/3 of character height
    General formula for character height
      Character height (mm) = D/200, where D = viewing distance (mm)
    Consider carefully the color combinations

## Slide 31: LABELS AND SIGNAGE
  Readability
    Avoid abbreviations wherever possible
    Increase readability of a block of letters or numbers by using borders or other embellishment techniques
    Locate the labels and signs where they will not be altered by painting or other routine maintenance
    Allow for access to labels and signs to be updated due to change in procedure, equipment, etc.

## Slide 32: WARNING SYSTEMS
In the event that a hazard associated with a
system cannot be eliminated through
engineering design, then there is a duty to
warn the users of the hazard.
Definition of Defect: a product or device is
considered defective if one of the following
conditions exist:
  Defective in design
  Defective in manufacturing
  Failure to adequately warn user of hazard

## Slide 33: WARNING SYSTEMS
  Key components
    Hazard alert symbol
    Signal word ( danger, warning, caution)
    Appropriate color code
    Pictograph or icon associated with hazard
    Hazard identification
    Consequences of ignoring hazard
    Method to avoid the hazard

## Slide 35: WARNING SYSTEMS
Warning Effectiveness
  Factors that can negatively influence the effectiveness of a warning
    User familiarity with the product
    Probability of mishap is perceived as low
    User in a hurry
    User is poorly motivated, fatigued or intoxicated
    Product is heavily “burdened” with many warnings, some of which seem inappropriate
    Product has active warnings that give frequent false alarms